## Slide 1: Flood Detection using Raspberry Pi
Presented By,
Mohammed Nauman Siddique
Department of Computer Science
OLD Dominion University
Spring 2021
2021-03-12

## Slide 2: Historical Flooding in Norfolk
1978
Nor'Easter
1998–1999
Hurricanes Bonnie and Floyd
2003
Hurricane Isabel
2006
Hurricane Ernesto
2009
Nor'easter Nor'Ida
2011
Hurricane Irene
2016
Hurricane Matthew
Reference: https://data.norfolk.gov/stories/s/FEMA-National-Flood-Insurance-Program-Redacted-Cla/gi5t-nkzw/

## Slide 3: Introduction for the Project
Measure flooding levels using the Raspberry PI board and alert users by turning on the LEDs.

## Slide 4: LED Lights Interpretation
LED Light | Water Level | Threat Level
Green | Low | Safe
Yellow | Medium | Alert
Red | High | Danger

## Slide 5: Results from the Project

## Slide 6: Equipment for the project
Fish Tank
Raspberry Pi Kit (3 or 4)
Raspberry Pi Camera
Bread Board
Three LED Lights (Red, Yellow, and Green)
Resistors (Minimum 3)
Jumper Wires

## Slide 7: Raspberry Pi Kit
Taken from: http://www.eleduino.com/Raspberry-Pi-3-Super-Integrated-Computer-Kit-p10572.html
Screen
Pi Case
Pi Board
Heat Sink
(Optional)
SD Card and
SD Card Reader (optional)
Power Adapter and cable
HDMI

## Slide 8: Raspberry Pi
Taken from: https://projects.raspberrypi.org/en/projects/raspberry-pi-getting-started/2

## Slide 9: How to power up your Pi board?
Insert SD Card into your Pi Board
Connect Pi Board to a monitor screen using HDMI Cable
Connect Mouse and Keyboard to the USB Ports
Power Up your Pi board

## Slide 10: Connect Pi Board to Internet
Connecting Pi Board to Wi-Fi using User Interface https://www.raspberrypi.org/documentation/configuration/wireless/desktop.md
Connecting Pi Board to Wi-Fi using CLI https://www.raspberrypi.org/documentation/configuration/wireless/wireless-cli.md
Connect Pi Board to LAN using Ethernet Port https://raspberrypi.stackexchange.com/questions/11684/how-can-i-connect-my-pi-directly-to-my-pc-and-share-the-internet-connection

## Slide 11: Pi Camera
Taken from: https://projects.raspberrypi.org/en/projects/getting-started-with-picamera

## Slide 12: How to connect Pi Camera to Pi Board
Power Off your Pi Board
Find the camera port on the Pi Board
Pull up the camera port plastic clip
Insert the Pi Camera ribbon and make sure the cable was inserted in the correct manner
Push the plastic clip back into place
Power Up your Pi Board
Reference: https://projects.raspberrypi.org/en/projects/getting-started-with-picamera/2

## Slide 13: Main Menu -> Raspberry Pi Configuration
Reference: https://projects.raspberrypi.org/en/projects/getting-started-with-picamera/2

## Slide 14: Interfaces -> Camera (Enabled)
Reference: https://projects.raspberrypi.org/en/projects/getting-started-with-picamera/2

## Slide 15: Bread Board
Taken from: https://learn.adafruit.com/breadboards-for-beginners?view=all

## Slide 16: Fish Tank Model
Land
Water
White Background

## Slide 17: Flood Detection Model Architecture

## Slide 18: Assumptions of the Project
capture 256 * 256 pixel images
project simulated on a fish tank
Use white background for the fish tank to avoid grey scale image conversion issues
captured images must capture the entire fish tank
more than 90% of the image must be the fish tank to reduce the surrounding noise for better results

## Slide 19: Code Snippet for capturing Images
camera = picamera.PiCamera() # Setup a Picamera Object
camera.resolution = (256, 256) #Capture 256*256 resolution images
camera.start_preview() # Open Camera Preview
time.sleep(2) # Freeze the preview for 2 seconds
camera.capture(os.path.join(os.getcwd(), "images", "testing", imageName)) # Capture images and write to a file location

## Slide 20: Menu of the Program

## Slide 21: 1.jpg file is not present

## Slide 22: Capture Image using Option 1

## Slide 23: Validate 1.jpg file

## Slide 24: Captured 21 testing images
We captured 21 training images using Option 1.
Full List of images: https://github.com/isaki001/PiCamUtils/tree/master/floodDetection

## Slide 25: Truth set of captured images Available at: https://github.com/isaki001/PiCamUtils/tree/master/floodDetection

## Slide 26: Training the model (Select three images, one for low, one for medium, and one for high water level)
Water Level Low
Water Level Medium
Water Level High

## Slide 27: Train the model using option 2

## Slide 28: Basic about Greyscale Images and Pixel Values
0
255
Image Height
in Pixels
0
255
Image Width
in Pixels
255
0

## Slide 29: Use the image to find pixel values of fish tank, land level, and water level
Step 1: Select a 256*256 image
Step 2: Convert it to Greyscale Image
Step 3: Find the fish tank top and bottom pixel values: tankTop and tankBottom
Step 4: Find the water level pixel value : waterLevel
Step 5: Find the highest point on the land pixel value : landLevel
Step 6: Compute scaling ratio (Tank Height / 255), since 255 is the height of image in pixel value
Tank Height = (tankTop – tankBottom)
Scaling Ratio = Tank Height / 255

## Slide 30: Computation of Fish Tank Pixel Values
0
255
Image Height
in Pixels
tankTop
tankBottom
landLevel
waterLevel

## Slide 31: Compute flood detection parameter values
Step 7: Compute Water Level Height
Water Height = (tankBottom - waterLevel) / Tank Height
Step 8: Compute Land and Water Height Difference
Land Height = (tankBottom - landLevel) / Tank Height
Height Difference = (Land Height – Water Height) / Tank Height
Step 9: Compute Water and Land Ratio
Water to Land Ratio = Water Height / Land Height

## Slide 32: Computed Training Values
Water Level | Water Height | Height Difference | Water to Land Ratio
Low | 0.035 | 0.227 | 0.134
Medium | 0.071 | 0.188 | 0.273
High | 0.145 | 0.165 | 0.468

## Slide 33
Write the training values to a serialized configuration object

## Slide 34: Configuration File (Low and Medium Water Levels) - Part 1
[LOW] // Stores low water level values
WATER: -1 // Water Height
DIFFERENCE: -1 // Height Difference
RATIO: -1 // Water Land Ratio
[MID]
WATER: -1
DIFFERENCE: -1
RATIO: -1

## Slide 35: Configuration File (Hight Water Level and LED Lights)
[HIGH]
WATER: 0.2
DIFFERENCE: 0.8
RATIO: -1
[LED] // Stores the Raspberry Pi GPIO Pin number for LED lights
RED: 4
YELLOW: 17
GREEN: 22

## Slide 36: Configuration File (Training Images)
[TRAINING] // Stores the training image names
LOW: low.jpg
MID: mid.jpg
HIGH: high.jpg

## Slide 37: Train the model using option 3

## Slide 38: How testing is done?
Step 1: Read the serialized Configuration object containing training values
Step 2: Compute Water Height, Height Difference, and Water to Land Ratio for the testing Image
Step 3: Compare the computed values against the training values of all the three parameters
Step 4: Each parameter returns a predicted water level
Step 5: Use the best of three water level as predicted water level
  Water Height: Red Height Difference: Yellow, Water to Land Ratio: Red  Predict: Red
Water Height: Red Height Difference: Yellow, Water to Land Ratio: Green  Predict: Error

## Slide 39: Testing Water Level Low

## Slide 40: Water Level Medium

## Slide 41: Testing Water Level High

## Slide 42: Results of the Project
Of the 21 Testing Images only one image is predicted with wrong water level.
Our model predicts testImage14.jpg as water level high while the actual water level is medium.

## Slide 43: Project Dependencies
Python3 (Programming Language)
picamera (library for capturing images using Raspberry Pi camera)
OpenCV (library for image processing)
gpiozero (library for using LEDs with Raspberry Pi)

## Slide 44: Project Code Description
.
├── images
│ ├── testing # Testing Images
│ ├── training # Training Images
├── watertank.py # Code for measuring water tank level and turning the respective LED lights
├── configmanagement.py # Read and writing configuration files
├── configuration
│ ├── config.ini # Configuration file
│ ├── config # Serialized Config object

## Slide 45
Code Available at: https://github.com/isaki001/PiCamUtils/tree/master/floodDetection

## Slide 46: Conclusion
Project for measuring the flooding levels using Raspberry PI by comparing images and turn on the respective LED to alert the user.
Project completed with a flood detection simulation model using Raspberry Pi with approx. 95% accuracy.