## Slide 1: Flood Detection using Raspberry Pi
Presented By,
Mohammed Nauman Siddique
Department of Computer Science
OLD Dominion University
Spring 2021
2021-04-05

## Slide 2: Timeline of Historical Flooding in Norfolk
1978
Nor'Easter
1998–1999
Hurricanes Bonnie and Floyd
2003
Hurricane Isabel
2006
Hurricane Ernesto
2009
Nor'easter Nor'Ida
2011
Hurricane Irene
2016
Hurricane Matthew
Reference: https://data.norfolk.gov/stories/s/FEMA-National-Flood-Insurance-Program-Redacted-Cla/gi5t-nkzw/

## Slide 3: Introduction for the Project
Measure flooding levels using the Raspberry PI board and alert users by turning on the LEDs.

## Slide 4: LED Lights Interpretation
LED Light | Water Level | Threat Level
Green | Low | Safe
Yellow | Medium | Alert
Red | High | Danger

## Slide 5: Results from the Project

## Slide 6: Equipment for the project
Fish Tank
Raspberry Pi Kit (3 or 4)
Raspberry Pi Camera
Bread Board
Three LED Lights (Red, Yellow, and Green)
Resistors (Minimum 3)
Jumper Wires

## Slide 7: Raspberry Pi Kit
Taken from: http://www.eleduino.com/Raspberry-Pi-3-Super-Integrated-Computer-Kit-p10572.html
Screen
Pi Case
Pi Board
Heat Sink
(Optional)
SD Card and
SD Card Reader (optional)
Power Adapter and cable
HDMI

## Slide 8: Raspberry Pi
Taken from: https://projects.raspberrypi.org/en/projects/raspberry-pi-getting-started/2

## Slide 9: How to power up your Pi board?
Insert SD Card into your Pi Board
Connect Pi Board to a monitor screen using HDMI Cable
Connect Mouse and Keyboard to the USB Ports
Power Up your Pi board

## Slide 10: Connect Pi Board to Internet
Connecting Pi Board to Wi-Fi using User Interface https://www.raspberrypi.org/documentation/configuration/wireless/desktop.md
Connecting Pi Board to Wi-Fi using CLI https://www.raspberrypi.org/documentation/configuration/wireless/wireless-cli.md
Connect Pi Board to LAN using Ethernet Port https://raspberrypi.stackexchange.com/questions/11684/how-can-i-connect-my-pi-directly-to-my-pc-and-share-the-internet-connection

## Slide 11: Pi Camera
Taken from: https://projects.raspberrypi.org/en/projects/getting-started-with-picamera

## Slide 12: How to connect Pi Camera to Pi Board
Power Off your Pi Board
Find the camera port on the Pi Board
Pull up the camera port plastic clip
Insert the Pi Camera ribbon and make sure the cable was inserted in the correct manner
Push the plastic clip back into place
Power Up your Pi Board

## Slide 13: Main Menu -> Raspberry Pi Configuration

## Slide 14: Interfaces -> Camera (Enabled)

## Slide 15: Bread Board
Taken from: https://learn.adafruit.com/breadboards-for-beginners?view=all

## Slide 16: Components for using a breadboard
Breadboard
LED lights (Red, Yellow, and Green)
Resistor (Atleast three)
Male-to-female jumper leads
Male-to-male jumper leads

## Slide 17: Connect LEDs using Breadboard to Pi Board
Power off the Pi Board
Connect a jumper wire from GPIO pins and breadboard voltage rail
Connect a jumper wires from GPIO pins and breadboard ground rail
Connect the LED to a terminal strip
Connect a resistor between voltage rail and LED terminal strip, if the LED strip is 5 connect resistor between terminal strip 5 and voltage rail
Connect a resistor between ground rail and LED terminal strip, if the LED strip is 5 connect resistor between terminal strip 5 and ground rail
Connect other LEDs by repeating the steps 2, 4, and 5.
Reference and further read: https://magpi.raspberrypi.org/articles/breadboard-tutorial

## Slide 18
Raspberry PI GPIO Pins
Reference: https://www.raspberrypi.org/documentation/usage/gpio/

## Slide 19: LEDs and its connection on breadboard
Positive Side (Anode)
Negative Side (Cathode)
Connect the Positive Side to the voltage rail of the breadboard
Connect the Negative Side to the ground rail of the breadboard
Reference: https://learn.sparkfun.com/tutorials/light-emitting-diodes-leds/all

## Slide 20: Fish Tank Model
Land
Water
White Background

## Slide 21: Flood Detection Model Architecture

## Slide 22: Assumptions of the Project
capture 256 * 256 pixel images
project simulated on a fish tank
Use white background for the fish tank to avoid grey scale image conversion issues
captured images must capture the entire fish tank
more than 90% of the image must be the fish tank to reduce the surrounding noise for better results

## Slide 23: Code Snippet for capturing Images
camera = picamera.PiCamera() # Setup a Picamera Object
camera.resolution = (256, 256) #Capture 256*256 resolution images
camera.start_preview() # Open Camera Preview
time.sleep(2) # Freeze the preview for 2 seconds
camera.capture(os.path.join(os.getcwd(), "images", "testing", imageName)) # Capture images and write to a file location

## Slide 24: Menu of the Program

## Slide 25: 1.jpg file is not present

## Slide 26: Capture Image using Option 1

## Slide 27: Validate 1.jpg file

## Slide 28: Captured 21 testing images
We captured 21 training images using Option 1.
Full List of images: https://github.com/isaki001/PiCamUtils/tree/master/floodDetection

## Slide 29: Truth set of captured images Available at: https://github.com/isaki001/PiCamUtils/tree/master/floodDetection

## Slide 30: Training the model (Select three images, one for low, one for medium, and one for high water level)
Water Level Low
Water Level Medium
Water Level High

## Slide 31: Train the model using option 2

## Slide 32: Greyscale Images and its usage in our project
Greyscale images are those images whose each pixel stores the shades of grey.
Advantage: Converting a RGB image requires less space for storing image pixel values in greyscale images
Usage in our project
For our project, we convert each image to a greyscale scale image using a threshold value. The pixel values in the image above the threshold is set to 255 while the pixel values below the threshold is set to 0.
The greyscale threshold values covert all the color pixels to 255 and all the white pixel to 0.

## Slide 33: Basic about Greyscale Images and Pixel Values
0
255
Image Height
in Pixels
0
255
Image Width
in Pixels
255
0

## Slide 34: Use the image to find pixel values of fish tank, land level, and water level
Step 1: Select a 256*256 image
Step 2: Convert it to Greyscale Image
Step 3: Find the fish tank top and bottom pixel values: tankTop and tankBottom
Step 4: Find the water level pixel value : waterLevel
Step 5: Find the highest point on the land pixel value : landLevel
Step 6: Compute scaling ratio (Tank Height / 255), since 255 is the height of image in pixel value
Tank Height = (tankTop – tankBottom)
Scaling Ratio = Tank Height / 255

## Slide 35: Computation of Fish Tank Pixel Values
0
255
Image Height
in Pixels
tankTop
tankBottom
landLevel
waterLevel
tankWidth

## Slide 36: Explanation of Fish Tank Values
tankTop is the pixel value of the first white pixel value encountered in the image.
tankBottom is the pixel value of the last white pixel value encountered in the image.
tankWidth is the maximum difference of pixel values between the first and last white pixel value encountered in the image on the horizontal scale.
landLevel is the pixel value where the black pixel value covers less than 80% of the fish tank and its pixel value is greater than tankTop.
waterLevel is the pixel value where the second half (tank split vertically) of the fish tank’s black pixel value covers between 30% and 43% of the fish tank.

## Slide 37: Compute flood detection parameter values
Step 7: Compute Water Level Height
Water Height = (tankBottom - waterLevel) / Tank Height
Step 8: Compute Land and Water Height Difference
Land Height = (tankBottom - landLevel) / Tank Height
Height Difference = (Land Height – Water Height) / Tank Height
Step 9: Compute Water and Land Ratio
Water to Land Ratio = Water Height / Land Height

## Slide 38: Computed Training Values
Water Level | Water Height | Height Difference | Water to Land Ratio
Low | 0.035 | 0.227 | 0.134
Medium | 0.071 | 0.188 | 0.273
High | 0.145 | 0.165 | 0.468

## Slide 39
Write the training values to a serialized configuration object

## Slide 40: Configuration File (Low and Medium Water Levels) - Part 1
[LOW] // Stores low water level values
WATER: -1 // Water Height
DIFFERENCE: -1 // Height Difference
RATIO: -1 // Water Land Ratio
[MID]
WATER: -1
DIFFERENCE: -1
RATIO: -1

## Slide 41: Configuration File (Hight Water Level and LED Lights)
[HIGH]
WATER: 0.2
DIFFERENCE: 0.8
RATIO: -1
[LED] // Stores the Raspberry Pi GPIO Pin number for LED lights
RED: 4
YELLOW: 17
GREEN: 22

## Slide 42: Configuration File (Training Images)
[TRAINING] // Stores the training image names
LOW: low.jpg
MID: mid.jpg
HIGH: high.jpg

## Slide 43: Train the model using option 3

## Slide 44: Testing Steps
Step 1: Read the serialized Configuration object containing training values
Step 2: Compute Water Height, Height Difference, and Water to Land Ratio for the testing Image
Step 3: Compare the computed values against the training values of all the three parameters
Step 4: Each parameter returns a predicted water level
Step 5: Use the best of three water level as predicted water level
  Water Height: Red Height Difference: Yellow, Water to Land Ratio: Red  Predict: Red
Water Height: Red Height Difference: Yellow, Water to Land Ratio: Green  Predict: Error

## Slide 45: Testing Water Level Low

## Slide 46: Water Level Medium

## Slide 47: Testing Water Level High

## Slide 48: Results of the Project
Of the 21 Testing Images only one image is predicted with wrong water level.
Our model predicts testImage14.jpg as water level high while the actual water level is medium.

## Slide 49: Project Dependencies
Python3 (Programming Language)
picamera (library for capturing images using Raspberry Pi camera)
OpenCV (library for image processing)
gpiozero (library for using LEDs with Raspberry Pi)

## Slide 50: Project Code Description
.
├── images
│ ├── testing # Testing Images
│ ├── training # Training Images
├── watertank.py # Code for measuring water tank level and turning the respective LED lights
├── configmanagement.py # Read and writing configuration files
├── configuration
│ ├── config.ini # Configuration file
│ ├── config # Serialized Config object

## Slide 51
Code Available at: https://github.com/isaki001/PiCamUtils/tree/master/floodDetection

## Slide 52: Conclusion
Project for measuring the flooding levels using Raspberry PI by comparing images and turn on the respective LED to alert the user.
Project completed with a flood detection simulation model using Raspberry Pi with approx. 95% accuracy.